# Introduction
This is the first lab not based on the book Getting Started with MicroPython. In this lab you are going to explore some of the common usages of capacitors in circuits. One use is to use an RC circuit to time events or set the oscillation time of a circuit. A second usage is to filter signals in frequency, and a third usage is to decouple DC, AC, and noise signals from each other. This covers a lot of territory, so let’s get started!
# Capacitors for Timing
Capacitors store charge and the basic formula is
V = Q over C	Eq. 1
where V is the voltage across a capacitor in Volts (abbreviated V), Q is the charge on the capacitor in Coulombs (abbreviated C), and C is the capacitance value in Farads (abbreviated F.) It turns out 1 F is a very large capacitor. The capacitors we will use are in the ranges of µF, nF, or pF. When a current runs into a capacitor, charge accumulates in it and the voltage across it increases. Consider the following circuit
Challenge:
Figure 1: A charging RC circuit. If Vc starts at zero when the switch is closed, the capacitor will charge and Vc will increase. Note 3.3V is also called Vcc.
If R = 100 kΩ and C = 100 μF, what will the initial current be?

What do you think the maximum Vc will be when the capacitor is fully charged?

## The Charge – Discharge Function
You should have seen the formula for a capacitor charging of discharging through a resistor
V(t) = V_0 +- V_1 e^{-t / %tau}	Eq. 2
where %tau = R C .
Challenge:
Find the value of τ in seconds for the Challenges above.

Find the values for V0 and V1 for the circuit in Figure 1 when the switch is closed.

You are going to make an oscillator. Wire up the circuit in Figure 2. You will drive the circuit with a digital output, and read VC with an ADC input. You need to write a program where it
- Turns on the digital output.to 1
- When VC = ⅔VCC, set the digital output to 0
- When VC = ⅓VCC, turn the digital output back 1.
- Repeat infinitely
Figure 3 shows what the waveform should look like, but ton and toff will be equal.
Figure 2: The oscillator circuit. GP28 is a digital output and GP26 is an ADC input.
Super Challenge:
- How long will it take the RC circuit to charge from ⅓VCC to ⅔VCC?
- What will T be in terms of R, C, and VCC?
- For R = 100 kΩ and C = 100 μF, what will T be?

Figure 3: The charge-discharge curve for the ocillator. You must make t_on and t_off equal.

## Working with Your Oscillator
1) Build the oscillator circuit with the components above, program the PicoW, and measure its frequency using an oscilloscope. In the space below, analyze your data and compare it to your calculated T. What is the percentage difference?

2) Change the components to make a 1 kHz oscillator. Is the result within the tolerance of the components?
Show your work below.

# To Continue …
The next lab is about using capacitors to filter signals in frequency. However, first you need to take a diversion to build a Function Generator. You will use it to make sine waves at different frequencies and measure how an RC filter affects that signal.
So now you will change gears to do the project Function Generator.

# Materials
- Pico W on a breadboard.